## Slide 1
Management
Interfaces in OpenBMC

## Slide 2: AGENDA
IPMI Overview
Redfish Overview
MCTP Overview
PLDM Overview
Protocol Comparison
Use Cases in OpenBMC

## Slide 3: IPMI
Legacy protocol for server management
Enables remote control of power, sensors, and logs
Works even when the main CPU is off (out-of-band management)
Uses KCS (local) and LAN (remote) for communication
Binary-based and hard to extend
Still supported in OpenBMC for compatibility
Lacks modern security (no encryption, weak auth)
Being replaced by modern alternatives like Redfish
Works with tools like ipmitool
OpenBMC runs an IPMI service (phosphor-ipmi-host)

## Slide 4: How IPMI Works in OpenBMC

## Slide 5: RedFISH
Modern, RESTful API for hardware management
Developed by DMTF to replace IPMI
Uses HTTPS + JSON for secure and human-readable communication
Enables access to:
Power and reset control
BIOS settings and firmware updates
Sensor monitoring and inventory
Fully supported in OpenBMC via bmcweb
Easily integrated with automation tools (Ansible, OpenStack, etc.)

## Slide 6: How Redfish Works in OpenBMC

## Slide 7: PLDM
Platform Level Data Model (by DMTF)
Structured, binary protocol used for platform management
Runs over MCTP transport layer
Replaces proprietary, vendor-specific protocols
Supports firmware updates, sensor monitoring, BIOS configuration
Enables standardized communication with devices like NICs, drives, etc.
Supported in OpenBMC for modern platform management

## Slide 8: PLDM Workflow in OpenBMC

## Slide 9: How PLDM Communicates via MCTP

## Slide 10: Comparison

## Slide 11: USE CASES
IPMI: System admin remotely powers ON/OFF a server using ipmitool over LAN via OpenBMC.
Redfish: Monitoring software queries Redfish API to check fan speeds and CPU temperature in JSON format.
PLDM: OpenBMC performs firmware update of a BIOS chip using PLDM over MCTP.
MCTP: BMC communicates with an NVMe drive over SMBus using MCTP to exchange PLDM sensor data.

## Slide 12
THANK YOU